## Slide 1: BS – 101 Engineering Physics
Lecture – 11
Engr. Safee Ullah

## Slide 2: Current, Drift Velocity and Current Density
Let’s reconsider the situation of a conductor as shown in figure.

## Slide 3: Current, Drift Velocity and Current Density (Contd.)
A conductor with cross-sectional area A and an electric field E directed from left to right. To begin with, we’ll assume that the free charges in the conductor are positive; then the drift velocity is in the same direction as the field.

## Slide 4: Current, Drift Velocity and Current Density (Contd.)
Suppose there are n moving charged particles per unit volume. Assume that all the particles move with the same drift velocity with magnitude 𝑣𝑑 . In a time interval 𝑑𝑡, each particle moves a distance 𝑣𝑑𝑑𝑡.

## Slide 5: Current, Drift Velocity and Current Density (Contd.)
The volume of the cylinder is A𝑣𝑑𝑑𝑡, and the number of particles within it is nA𝑣𝑑𝑑𝑡. If each particle has a charge q, the charge 𝑑𝑄 that flows out of the end of the cylinder during time 𝑑𝑡 is
𝑑𝑄 = 𝑞(nA𝑣𝑑𝑑𝑡) = 𝑛𝑞𝑣𝑑𝐴 𝑑𝑡

## Slide 6: Current, Drift Velocity and Current Density (Contd.)
And the current is
𝑑𝑡
𝑑
𝐼 = 𝑑𝑄 = 𝑛𝑞𝑣 𝐴
The current per unit cross-sectional area is called the current density J:
𝐴
𝐽 = 𝐼 = 𝑛𝑞𝑣
𝑑
𝐴
The units of current density are amperes per square meter ( ).
𝑚2

## Slide 7: Current, Drift Velocity and Current Density (Contd.)