## Slide 2: Network Coding for Wireless Applications: A Review
PPRESENTED BY:
HUZAIFA SHAHBAZ (21-CE-009)
AQSA SHAH(21-CE-039)
PRESENTED TO:
MAAM SOBIA ARSHAD

## Slide 3: OUTLINES
ABSTRACT
INTRODUCTION
LITERATURE REVIEW/BACKGROUND
Theoretical Foundations of Network Coding
Network Coding Techniques for Wireless Applications
Performance Analysis and Metrics
Applications in Wireless Networks
Challenges and Limitations
Recent Advances and Future Directions
Conclusion

## Slide 4: ABSTRACT
In this project our topic is Network coding for wireless applications: A review in this paper our focused on the following are:
Network coding is a technology that allows intermediate nodes to perform algebraic operations on incoming data streams, enabling networks to achieve theoretical capacity limits while providing enhanced robustness and efficiency.
The mathematical framework operates on finite field operations, with information-theoretic bounds determined through minimum cut analysis.
Various network coding techniques, such as Random Linear Network Coding (RLNC), Analog Network Coding (ANC), and Physical Layer Network Coding (PNC), provide different trade-offs between complexity and performance.
Performance analysis metrics include throughput gains, delay characteristics, energy consumption, and reliability measures across different wireless scenarios.
Network coding finds applications in cellular networks, WSNs, MANETs, VANETs, and satellite systems.
Current limitations include computational complexity, security vulnerabilities, and implementation challenges.
Future research should focus on machine learning integration, quantum applications, and 6G system integration.

## Slide 5: ABSTRACT
The fifteen research papers from our projects consist of following are:
Energy-efficient linear network coding in wireless sensor networks.by Li, X., Zhang, Y., & Wang, J. (2020).
Adaptive network coding for vehicular ad hoc networks: A mobility-aware approach by Zhao, L., & Chen, M. (2021).
Random linear network coding for delay-tolerant wireless networks: Performance analysis and optimization by Wang, S., Liu, H., & Kumar, A. (2022).
MQTT-based network coding for IoT applications in smart agriculture by Ahmed, R., Hassan, M., & Ali, S. (2023).
Machine learning-enhanced network coding for wireless mesh networks: A hybrid approach by Kim, J., & Yu, H. (2024).
Network information flow by Ahlswede, R., Cai, N., Li, S. Y. R., & Yeung, R. W. (2000).
Physical layer network coding in two-way relay channels: Performance analysis and optimization by Chen, L., Wang, X., & Zhang, H. (2020).
Secure network coding for wireless sensor networks: A comprehensive survey by Kumar, V., Singh, A., & Gupta, R. (2021).
Energy-aware random linear network coding for mobile ad hoc networks by Patel, M., & Johnson, K. (2021).
Network coding for 5G and beyond: Challenges and opportunities by Thompson, D., Brown, S., & Williams, J. (2022).
Quantum network coding: Fundamentals and applications in wireless systems by Rodriguez, C., & Martinez, P. (2022).
Deep learning approaches for adaptive network coding in wireless networks by Davis, A., & Wilson, E. (2023).
Distributed network coding for massive IOT networks by Nakamura, T., & Yamamoto, K. (2023).
A comprehensive analysis of network coding for efficient wireless network communication by Kumar, A., & Sharma, P. (2023).
Reinforcement learning-based network coding for dynamic wireless environments by Anderson, M., & Taylor, L. (2024).

## Slide 6: Introduction
Traditional Wireless Networks:
"Store-and-forward" principle.
Poor utilization of network resources.
Challenges: broadcast nature, interference, limited bandwidth.
Introduction of Network Coding (Ahlswede et al., 2000):
Intermediate nodes combine data streams algebraically.
Breaks the traditional paradigm.
Fundamental Change & Benefits:
Achieves theoretical maximum information flow (max-flow min-cut theorem).
Added benefits: robustness, security, energy efficiency.

## Slide 7: LITERATURE REVIEW/BACKGROUND
Network coding (NC) has become a crucial approach for improving the efficiency of data transmission, throughput, and resilience in wireless networks.
Li et al. (2020) suggested a linear network coding approach that was implemented in WSNs to enhance energy efficiency. By encoding data at intermediate nodes and minimizing retransmissions, the network was able to achieve higher throughput while maintaining lower latency.
Zhao & Chen (2021) delved into the concept of adaptive network coding (ANC) for VANETs. Their simulation-based approach demonstrated that ANC improved packet delivery under changing mobility conditions, guaranteeing quality of service in real-time vehicular applications.
Wang et al. (2022) examined the influence of random linear network coding (RLNC) in delay-tolerant networks (DTNs). Their analytical model demonstrated improved resilience to packet loss in networks that experience intermittent connectivity.
Ahmed et al. (2023) examined the use of NC in internet of things (iot) environments, with a focus on its application in smart agriculture. The research combined NC with MQTT protocols, demonstrating improved reliability and energy efficiency.
Kim & Yu (2024) suggested a hybrid approach that combines both non-cooperative and machine learning techniques for wireless mesh networks. Their approach anticipated network states and dynamically adjusted coding strategies, resulting in enhanced throughput and adaptability.

## Slide 8: LITERATURE REVIEW/BACKGROUND
Year | Title | Summary(Methodology) | Findings | Strengths | Gaps/Weakness | Evaluated parameters
2020 | Li et al. – “Energy-Efficient Linear Network Coding in WSNs | Model-based method employing linear NC to minimize retransmissions. | Enhanced resource utilization and productivity. | Optimized Code, Minimal Delay. | Expensive computational expense at nodes in between. | Energy consumption, latency, throughput
2021 | Zhao & Chen – “Adaptive Network Coding for VANETs” | Adaptive NC with Mobility-Aware Models in NS-3 Simulator. | Improved data transmission rates in dynamic environments. | Dynamic adaptability | Insufficient empirical evidence. | Packet Delivery Rate, Transit Time, Network Effectiveness.
2022 | Wang et al. – “RLNC for Delay-Tolerant Wireless Networks” | Computational modeling and Monte Carlo simulations. | Enhanced dependability in networks with limited connectivity. | Robust under packet loss | Performance not evaluated. | Reliability, delay, data excess
2023 | Ahmed et al. - "MQTT-based network coding for IOT" | NC integrated with MQT in Smart Agriculture IOT | Increased reliability and energy savings | Real world IoT application | Limited scalability analysis | Use of energy, reliability, data throughput
2024 | Kim and U-"ML-operated NC in Wireless Aries Network" | Hybrid ML-NC approach using reinforcement learning | Adaptive coding enhances the efficiency of data processing. | Guessable adaptability | High overhead and model training complexity | This is about the factors such as throughput, adaptability, and network load.

## Slide 9: Theoretical Foundations of Network Coding
Core Principle: Information can be added at intermediate nodes to improve performance.
Linear Algebra on Finite Fields:Network represented as a graph g=(V,E).
Coding operation: ye=∑(ae,e′×xe′)ye: output symbol on edge e
xe′: input symbols on incoming edges
ae,e′: coding coefficients from a finite field
Finite Field Operation:Usually on GF(2^m).
Operations performed modulo an irreducible polynomial.
Ensures reversibility and original information recovery.

## Slide 10: Network Coding Techniques for Wireless Applications
Random Linear Network Coding (RLNC):Most widely studied form.
Coding coefficients chosen randomly from a finite region.
Major Benefits:Distributed Implementation: No centralized coordination needed.
Adaptability: Works well with dynamic topologies.
Robustness: Provides inherent error correction.
Implementation Details:Each coded packet contains:Coding vector (linear combination).
Payload (actual coded data).
Generation identifier (for packet grouping).
Decoding Process:Receivers collect linearly independent combinations.
Solve for original data using Gaussian elimination.

## Slide 11: Performance Analysis and Metrics
Error Resilience:NC provides inherent error correction capabilities.
Minimum distance of the code determines error correction.
dmin=minwt(c):c∈C,c≠0
Packet Loss Recovery:NC can recover from packet losses without retransmissions.
Requires sufficient coded packets to be received.

## Slide 12: Applications in Wireless Networks
Multicast/Broadcast Services:
Significantly improves efficiency in cellular multicast.
Examples: Mobile TV Broadcasting, Software Updates, Content Distribution.
Implementation in LTE/5G:
eMBMS: Uses NC for efficient multicast.
Coordinated Multipoint (CoMP): NC enhances cooperation between base stations.
Device-to-Device (D2D) Communication: Coding improves relay efficiency.
Performance Gains:
2-3x improvement in multicast efficiency.
30-40% reduction in transmission power.

## Slide 13: Challenges and Limitations
Practical Implementation Process:Synchronization: Generation boundaries, timing synchronization, buffer management.
Security Concerns:Pollution Attacks: Malicious nodes injecting corrupted packets.
Eavesdropping: Increased vulnerability to passive attacks.
Byzantine Behavior: Dealing with malicious coding operations.
Standardization Issues: Protocol Integration, Interoperability, Backward Compatibility.

## Slide 14: Recent Advances and Future Directions
Machine Learning Integration:AI-Enabled Network Coding:Deep Learning for Code Design (Neural Networks, Reinforcement Learning).
Federated Learning for distributed learning.
Intelligent Resource Allocation: Predictive Coding, Dynamic Adaptation, Traffic Prediction.
Performance Improvements: 20-30% throughput, 40% delay reduction.
Quantum Network Coding:Quantum Information Theory: Extending NC to quantum systems.Quantum Entanglement, Quantum Error Correction, Quantum Communication Networks.
Potential Applications: Quantum Internet, Quantum Cryptography, Quantum Sensing.

## Slide 15: Conclusion
Summary of Impact: Network coding has significantly improved wireless communication.
Key Enhancements: Throughput, robustness, and spectrum efficiency.
Superiority: Outperforms traditional routing in multicast and cooperative scenarios.
Versatility: Various coding techniques (linear, analog, opportunistic) suitable for real-world environments.
Future Outlook:Despite implementation challenges, advancements in hardware and software support deployment.
Scalability and adaptability confirmed for evolving wireless standards (IoT, MANETs, 5G).

## Slide 16: REFERENCES
Fragouli, C., & Soljanin, E. (2007). Network coding fundamentals. Foundations and Trends in Networking, 2(1), 1-133.
Ho, T., Médard, M., Koetter, R., Karger, D. R., Effros, M., Shi, J., & Leong, B. (2006). A random linear network coding approach to multicast. IEEE Transactions on Information Theory, 52(10), 4413-4430.
Kschischang, F. R., & Romo, S. (2007). Coding for errors and erasures in random network coding. IEEE Transactions on Information Theory, 54(8), 3579-3591.
Chachulski, S., Jennings, M., Katti, S., & Katabi, D. (2007). Trading structure for randomness in wireless opportunistic routing. ACM SIGCOMM Computer Communication Review, 37(4), 169-180.
Nazer, B., & Gastpar, M. (2011). Compute-and-forward: Harnessing interference through structured codes. IEEE Transactions on Information Theory, 57(10), 6463-6486.
Lucani, D. E., Médard, M., & Stojanovic, M. (2010). Systematic network coding for time-division duplexing. IEEE Transactions on Communications, 58(8), 2321-2331.